## Slide 1: The impact of SO2 emission from China on Japan
Environmental Science / Chen Gu
May 13, 2014
Notes: Good afternoon ,everyone. I am very happy to give my presentation here. My name is Chen Gu ,and my major is environmental science. The presentation I’ll show to you here is The impact of SO2 (sulfur dioxide)emission from China on Japan .

## Slide 2: CONTENTS
Model
Data
Method
Result
Notes: My presentation contains four parts, the Model, Data, Method and final Result.

## Slide 3: East Asia
Notes: The picture showed here is the map of East Asia. It’s a brief overview of our work base.

## Slide 4: Sub-regions of China
Fig. 1. Seven sub-regions of China
Notes: In order to easy comprehension and comparison, we divide China area into 7 sub-regions as showed in figure 1. These sub-regions are the North, Northeast, East, Central, South, Southwest and Northwest China.

## Slide 5: Model
three-dimensional， regional-scale， CTM
horizontal resolution （24km  24 km）
12 vertical layers (1.5m, 3.9m, 10m, 100m, 350m, 700m, 1200m, 2000m, 3000m, 5000m ,7000m)
CanMETOP
Ma J, Daggupaty SM, Harner T, Li Y (2003) Impacts of lindane usage in the Canadian prairies on the Great Lakes ecosystem – 1: coupled atmospheric transport model and modeled concentrations in air and soil. Environ Sci Technol 37:3774–3781
Notes: In this study ,we use Canadian model. CanMETOP is a three-dimensional regional-scale atmospheric chemical transport models.
This model has a horizontal resolution of 24km  24 km and
12 vertical layers (centered at 1.5, 3.9, 10, 100, 350, 700, 1200, 2000, 3000, 5000 and 7000m, representatively) .
we can get more information from this paper.
Canadian Model for Environmental Transport of Organochlorine Pesticides

## Slide 6
Fig. 2. SO2 Emission in China (2007，mg km-2 s-1)
Emission data
1
2
Validation data
1.PKU-SO2-China
2.INTEX-B for Japan/Mongolia/Korea
Data
Notes: Turning to the next part. The Data is comprised of Emission data and Validation data . Emission data includes the SO2 emission
Of china in 2007 and the INTEX-B for Japan ,Mongolia and Korea .we scaled this emission data to keep consistent with China.

## Slide 7: Data
Emission data
1
2
Validation data
Chart: Observed, μg m-3
| 31.904294354838711 | 28.880670362903228 | 16.618902889784948 | 3.0629637125391436 | 2.2204627159813004 | 1.2979475570944621 | 1.0300018234419928 | 2.5314753301466002 | 0.96422209951236348 | 1.6316105876990532 | 1.4611648043102894 | 5.9391515479048875 | 3.1038137183254038 | 5.9850000000000003 | 7.5366666666666662 | 5.541666666666667 | 10.94972375 | 3.3209822916666667
 | 27.5524 | 48.2668 | 16.5556 | 0.87394 | 2.329 | 0.87411 | 1.0414 | 1.3996 | 0.6402 | 1.2515 | 1.4286 | 5.3257 | 3.1884 | 3.0698 | 6.6898 | 5.7885 | 10.7618 | 1.5467
 | 0.1 | 100
Fig. 3. Modeled and observed annual mean SO2 concentration at 18 monitoring sites of EANET
Notes: CanMETOP was run with this compiled emission inventory. The results were extracted for comparison with observation data at 18 monitoring sites of Acid Deposition Monitoring Network in East Asia (EANET).The SO2 annual mean concentration at 18 monitoring sites of EANET was Modeled and observed. From this figure, we can find the balance between modeled and observed data.For annual average, more than two-thirds sites were closed to 1:1 line.

## Slide 8
Residual
The influence of A0 to B =
Method
Notes: We used the Residual method to calculate. The equation is here, and the final results is the most important part in my presentation today.

## Slide 9
Chart: SO2 column concentration of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.19585 | 0.15121 | 0.27156 | 0.080656 | 0.010254 | 0.032831 | 0.026951 | 0.18719 | 0.0025339 | 0.040963
summer | 0.084768 | 0.060217 | 0.2672 | 0.065094 | 0.015271 | 0.0052381 | 0.010918 | 0.42843 | 0.0003328 | 0.062525
autumn | 0.15661 | 0.098522 | 0.17335 | 0.046773 | 0.0015566 | 0.020413 | 0.043079 | 0.41607 | 0.0026736 | 0.04096
winter | 0.17938 | 0.097217 | 0.3072 | 0.13057 | 0.012001 | 0.089073 | 0.060897 | 0.091682 | 0.0030112 | 0.028974
annual | 0.16888 | 0.10613 | 0.27574 | 0.099193 | 0.010576 | 0.055934 | 0.044123 | 0.19931 | 0.0025236 | 0.03759
column concentration
1
2
deposition
3
ground concentration(<100m)
Result
Notes: The first part is about the column concentration. Here we see, to study the impact of SO2 emissions from China on Japan, the annual mean columns of SO2 were significantly different over space. The North and East China were the high emission area. The Japan SO2 influence caused by inner emission was much bigger than China emission. The impacts of Mongolia and Korea were almost invisible.

## Slide 10: Result
column concentration
1
Chart: Sulfate column concentration of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.26331 | 0.13423 | 0.30346 | 0.12269 | 0.010598 | 0.065323 | 0.049509 | 0.02439 | 0.0049851 | 0.021513
summer | 0.20671 | 0.08021 | 0.43384 | 0.12353 | 0.02839 | 0.0173 | 0.032623 | 0.03482 | 0.0022903 | 0.040282
autumn | 0.26927 | 0.089141 | 0.25042 | 0.085587 | 0.0029578 | 0.043536 | 0.16007 | 0.066414 | 0.0063323 | 0.026278
winter | 0.19505 | 0.051554 | 0.30252 | 0.17046 | 0.014359 | 0.15251 | 0.090044 | 0.0090749 | 0.0038324 | 0.01059
annual | 0.2253 | 0.089293 | 0.36056 | 0.12672 | 0.018983 | 0.053849 | 0.060557 | 0.031723 | 0.0036412 | 0.029373
Notes: On the contrary, the influence of Sulfate column concentration from China to Japan is much bigger than the influence caused by Japan itself. The conclusion is that, the impact from China on Japan is mainly through Sulfate column concentration .

## Slide 11: Result
Chart: SO2 ground concentration of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.031556 | 0.038824 | 0.034381 | 0.0049308 | 9.3393e-05 | 0.00055458 | 0.0013852 | 0.85944 | 0.00038597 | 0.028448
summer | 0.005133 | 0.0044367 | 0.033337 | 0.0046054 | 0.00070557 | 0.00026842 | 0.00063271 | 0.93461 | 2.0707e-05 | 0.016249
autumn | 0.013608 | 0.01499 | 0.0099936 | 0.0020035 | 6.7465e-05 | 0.00045627 | 0.0020461 | 0.93667 | 0.0002308 | 0.019936
winter | 0.062568 | 0.059859 | 0.093464 | 0.02094 | 0.0006119 | 0.0089106 | 0.0087345 | 0.69777 | 0.0010484 | 0.046094
annual | 0.028923 | 0.03009 | 0.044489 | 0.0084916 | 0.00038792 | 0.0027058 | 0.0033154 | 0.85309 | 0.00043369 | 0.028077
column concentration
1
deposition
3
2
ground concentration(<100m)
Notes: Then, let’s talk about the SO2 ground concentration.
We can see clearly that the influence from itself is much bigger than from China. So, We can ignore the impact of China.

## Slide 12: Result
2
Chart: Sulfate ground concentration of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.24114 | 0.20307 | 0.23752 | 0.0431 | 0.0005934 | 0.006953 | 0.013479 | 0.19433 | 0.0039728 | 0.055838
summer | 0.1562 | 0.065987 | 0.39414 | 0.083112 | 0.02238 | 0.010751 | 0.022798 | 0.17812 | 0.0016053 | 0.064907
autumn | 0.198 | 0.10429 | 0.12299 | 0.035745 | 0.00091537 | 0.012437 | 0.084263 | 0.3803 | 0.0045335 | 0.056529
winter | 0.23137 | 0.11871 | 0.32345 | 0.093482 | 0.0023579 | 0.055868 | 0.047413 | 0.084297 | 0.0045729 | 0.038477
annual | 0.18979 | 0.10771 | 0.31867 | 0.070149 | 0.012418 | 0.016095 | 0.031144 | 0.19273 | 0.0028624 | 0.058424
ground concentration(<100m)
Notes: On the other hand, the influence of Sulfate ground concentration from China on Japan was the main reason.
We can also find that the impact of ground concentration is much less than column concentration .

## Slide 13: Result
Chart: Total sulfur deposition of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.1556 | 0.081345 | 0.28957 | 0.10979 | 0.01583 | 0.054353 | 0.030853 | 0.23602 | 0.0024802 | 0.024171
summer | 0.15832 | 0.055526 | 0.39845 | 0.11712 | 0.027417 | 0.014097 | 0.025035 | 0.16834 | 0.001486 | 0.034204
autumn | 0.13378 | 0.069509 | 0.12555 | 0.03192 | 0.0028466 | 0.013013 | 0.064593 | 0.52978 | 0.0024855 | 0.026528
winter | 0.14339 | 0.076149 | 0.29269 | 0.11457 | 0.017096 | 0.074385 | 0.041877 | 0.20994 | 0.0022103 | 0.027698
annual | 0.15172 | 0.067502 | 0.32035 | 0.10554 | 0.019802 | 0.036445 | 0.034409 | 0.23262 | 0.0019795 | 0.029637
column concentration
1
deposition
3
2
ground concentration(<100m)
Notes: Thirdly, this chart was about the sulfur deposition. From the annual mean data, the SO2 emissions from China on Japan were also varied significantly over space. The high emissions were in North and East China. The sulfur deposition from Japan itself is more serious than from China. The impact of Mongolia and Korea can be ignored.

## Slide 14: Result
deposition
3
Chart: Sulfur dry deposition of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.045456 | 0.048747 | 0.049612 | 0.0081405 | 0.00016043 | 0.0012903 | 0.0023045 | 0.81745 | 0.00065299 | 0.026187
summer | 0.02973 | 0.014108 | 0.085455 | 0.016234 | 0.0039684 | 0.00189 | 0.0040659 | 0.82463 | 0.00028936 | 0.01963
autumn | 0.021561 | 0.017816 | 0.014419 | 0.0035882 | 0.00014148 | 0.0010377 | 0.0063069 | 0.91664 | 0.00043279 | 0.018052
winter | 0.06179 | 0.055018 | 0.090278 | 0.021413 | 0.00068839 | 0.010081 | 0.0096347 | 0.71096 | 0.0010684 | 0.039074
annual | 0.039378 | 0.033084 | 0.062137 | 0.012703 | 0.0014086 | 0.0035189 | 0.0054726 | 0.81619 | 0.00059232 | 0.025518
Notes: This is Sulfur dry deposition . We can see that the influence from Japan itself is much bigger than from China. so, We can ignore the impact of Sulfur dry deposition from China.

## Slide 15: Result
deposition
3
Chart: Sulfur wet deposition of Japan
| NorthChina | NortheastChina | EastChina | CentralChina | SouthChina | SouthwestChina | NorthwestChina | Japan | mongolia | korea
spring | 0.18224 | 0.089231 | 0.34761 | 0.13438 | 0.01962 | 0.06719 | 0.03776 | 0.095361 | 0.0029222 | 0.023683
summer | 0.17655 | 0.061399 | 0.44284 | 0.13143 | 0.030742 | 0.015829 | 0.028009 | 0.075277 | 0.0016557 | 0.036271
autumn | 0.20143 | 0.10067 | 0.19253 | 0.048997 | 0.0044772 | 0.020231 | 0.099725 | 0.29659 | 0.0037227 | 0.031637
winter | 0.164 | 0.081485 | 0.3438 | 0.13809 | 0.02124 | 0.090625 | 0.05002 | 0.083408 | 0.0024987 | 0.024825
annual | 0.17722 | 0.075315 | 0.37896 | 0.12661 | 0.023977 | 0.04392 | 0.040978 | 0.10015 | 0.0022944 | 0.030572
Notes: Finally, although the influence of Sulfur wet deposition from China is much bigger than from Japan itself ,the impact of wet deposition is still much less than Japan own Sulfur dry deposition .

## Slide 16: Conclusion
1. The impact is mainly through sulfate column concentration.
2. the impact of ground concentration is much less.
4. The impact is mainly through sulfur wet deposition.
3. The impact mainly come from North China and East China.
Notes: The last slide is a brief summary of my presentation.
The first part showed that the impact of SO2 emission from China on Japan is mainly due to Sulfate column, Which was proved to be less important than ground concentration in part 2. The third part introduced the mainly impact came from the North and East China. And finally, the impact of deposition from China to Japan is mainly through Sulfur wet deposition.

## Slide 17
Author Chen Gu
Email pkugchen@pku.edu.cn
Department of Environmental Science
School of Urban and Environmental Sciences
Peking University
THANK YOU
Notes: That’s all ,thank you for your attention.