## Slide 1
Stable carbon isotopes to monitor CO2 source mix in the urban environment
F. R. Vogel, L. Wu, J-L. Bonne, M. Ramonet, G. Broquet,, P. Ciais, L. Huang and D. Worthy
Laboratoire des Sciences Du Climat et de L‘Environment, Gif-sur-Yvette, France
Environment Canada, Climate Research Division, Toronto, Canada

## Slide 2
Urban areas are responsible for 67% of global primary energy consumption and 71% of global energy related (≈ fossil fuel) CO2 emissions (IEA, 2008)…
..the urban contribution to CO2 emissions from primary energy use is predicted to rise to 76% globally in 2030 (Dhakal, 2010).
City-scale emissions

## Slide 3
 | EDGAR V4 | IER 2005 | AIRPARIF2008 | Max – Min
Resolution | 0.1° x 0.1° | 1min x 1min | 1km x 1km | 
Annual budget of Ile-de-France (TgC) |  |  |  | 
Residential | 6.75 | 5.36 | 7.80 | 31%
Road | 8.50 | 6.03 | 3.37 | 60%
Industry | 5.19 | 4.61 | 3.09 | 42%
Total | 24.65 | 16.39 | 14.26 | 50%
Courtesy: Lin Wu
(km-scale, hourly)
Inconsistencies
<10%
>50%
(Developed countries, annual total)
« Uncertainty » of city-scale emissions

## Slide 4
Uncertainty in temporal emission factors
Potential bias for selected data sets (flasks, satellites, inversion using pm only)
Temporal variation of fossil fuel CO2 emissions

## Slide 5
>100 Million $ - retrofitting of houses and city facilities (2007)
800 Million $ - renewal of TTC bus fleet to diesel-hybrids, etc (2005-2009)
Bike lanes from 300km to 1000km until 2012
Green roof program ongoing
(Phasing out of coal power plants in Ontario)
http://www.toronto.ca/environment/

## Slide 6
Residential
Road traffic
Industrial
Background + Fossil fuel + Bio = Total
d13C in CO2 in different source sectors

## Slide 7
Data from Environment Canada, ICF International and City of Toronto
Natural Gas
Liquid fuels
Solid fuels
d13C in CO2 in different source sectors

## Slide 8
Data from Environment Canada, ICF International and City of Toronto
Natural Gas
Liquid fuels
Solid fuels
Carbon-13
-44‰ to -48‰
-27‰ to -28‰
-24‰ to -27‰
Biogenic CO2
C3: -20‰ to -30‰
C4: -10‰ to -15‰
d13C in CO2 in different source sectors

## Slide 9
Southern Ontario, Canada
d13C in CO2 observations in Toronto, Canada

## Slide 10
Chart: 
Chart: 
d13C in CO2 observations in Toronto, Canada

## Slide 11
Drift disappears after calibration
Typical precision ca. 0.2 permil for 15min averages
d13C in CO2 observations in Toronto, Canada

## Slide 12
Drift disappears after calibration
Typical precision ca. 0.2 permil for 15min averages
Chart: 
Instrument performance 2014
d13C in CO2 observations in Toronto, Canada

## Slide 13
Chart: 
Chart: 
d13C in CO2 observations in Toronto, Canada

## Slide 14
Chart: 
Chart: 
observations
Simple mixing calculation (keeling plot) reveals mean source signature
d13C source signatures in Toronto

## Slide 15
Chart: Date [d/m/a]
Seasonal cycle - d13C source signatures in Toronto
Clear seasonal cycle in source signature

## Slide 16
Chart: Date [d/m/a]
Winter contribution: Bio 0.05, coal 0.1, liquid 0.225, gas 0.675
Summer contribution: Bio 0.4, coal 0.2, liquid 0.3, gas 0.1
Seasonal cycle - d13C source signatures in Toronto

## Slide 17
Chart: Date [d/m/a]
Winter contribution: Bio 0.05, coal 0.1, liquid 0.225, gas 0.675
Summer contribution: Bio 0.4, coal 0.2, liquid 0.3, gas 0.1
Seasonal cycle - d13C source signatures in Toronto
Are diurnal variations systematic?

## Slide 18
Data from Environment Canada, ICF International and City of Toronto
Natural Gas
Liquid fuels
Solid fuels
Carbon-13
-44‰ to -48‰
-27‰ to -28‰
-24‰ to -25‰
Biogenic CO2
C3: -20‰ to -30‰
C4: -10‰ to -15‰
Winter
d13C source signatures in Toronto, Canada

## Slide 19
Chart: Time of day (hours) UTC
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
 | -36.6591 | -37.1115 | -39.2674 | -37.0605 | -37.9306 | -37.9047 | -38.8802 | -38.8144 | -41.1107 | -38.0574 | -39.6081 | -40.4229 | -39.2252 | -38.1525 | -40.9172 | -40.2225 | -40.2561 | -39.6543 | -39.1179 | -38.041 | -40.4774 | -37.9921 | -37.1508 | -36.6911 | -36.6591 | -37.1115 | -39.2674 | -37.0605 | -37.9306 | -37.9047 | -38.8802 | -38.8144 | -41.1107 | -38.0574 | -39.6081 | -40.4229 | -39.2252 | -38.1525 | -40.9172 | -40.2225 | -40.2561 | -39.6543 | -39.1179 | -38.041 | -40.4774 | -37.9921 | -37.1508 | -36.6911
daytime
Diurnal cycle (winter) - d13C source signatures in Toronto
Data selected: DCO2 >20ppm, R2>0.9 -> typically 15-20 point per hour bin
Clear daily cycle for winter data (Jan&Feb)
daytime

## Slide 20
daytime
Chart: Time of day (hours) UTC
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
 | -36.6591 | -37.1115 | -39.2674 | -37.0605 | -37.9306 | -37.9047 | -38.8802 | -38.8144 | -41.1107 | -38.0574 | -39.6081 | -40.4229 | -39.2252 | -38.1525 | -40.9172 | -40.2225 | -40.2561 | -39.6543 | -39.1179 | -38.041 | -40.4774 | -37.9921 | -37.1508 | -36.6911 | -36.6591 | -37.1115 | -39.2674 | -37.0605 | -37.9306 | -37.9047 | -38.8802 | -38.8144 | -41.1107 | -38.0574 | -39.6081 | -40.4229 | -39.2252 | -38.1525 | -40.9172 | -40.2225 | -40.2561 | -39.6543 | -39.1179 | -38.041 | -40.4774 | -37.9921 | -37.1508 | -36.6911
daytime
Relativ emission strength: liquid vs gas (1:3) and (1:1)
Emissions for bio assumed below 5% and coal fixed at 10% (inventory and aerosols)
Diurnal cycle (winter) - d13C source signatures in Toronto

## Slide 21
Influence of remote sources on the urban environment

## Slide 22
Influence of remote sources on the urban environment

## Slide 23
Atmospheric transport model suggests sources from Germany could/should contribute
Influence of remote sources on the urban environment

## Slide 24
Chart: d13C in CO2 (permil raw)
Chart: 12CO2 (ppm dry raw)
Strong signals in d13C anti-correlated with CO2 concentration
Isotopes CAN reveal emission source
Influence of remote sources on the urban environment

## Slide 25
Chart: 
Monthly source signature Southern Germany: (Kaul, 2007): -26 ‰ to -31 ‰
Source signature of Paris Winter 2010 (Lopez et al. 2013): -36 ‰ to -39 ‰
Influence of remote sources on the urban environment

## Slide 26
Urban environments are complex, and they account for the majority of fossil fuel CO2 emissions
d13C is a fuel specific proxy
We can trace seasonal changes in the sources mix and diurnal cycle of sources (in winter)
Source signature can help to identify remote sources…
…but better constraints on sources needed to constrain emissions more precisely
Model framework (transport and inventory) needed for better interpretation of signals… under development!
Summary of d13C in CO2 in the urban environment

## Slide 27
Urban environments are complex, and they account for the majority of fossil fuel CO2 emissions
d13C is a fuel specific proxy
We can trace seasonal changes in the sources mix and diurnal cycle of sources (in winter)
Source signature can help to identify remote sources…
…but better constraints on sources needed to constrain emissions more precisely
Model framework (transport and inventory) needed for better interpretation of signals… under development!
Summary of d13C in CO2 in the urban environment
Thank you

## Slide 28
Data from Environment Canada, ICF International and City of Toronto
Natural Gas
Liquid fuels
Solid fuels
Carbon-13
-44‰ to -48‰
-27‰ to -28‰
-24‰ to -25‰
Sensitivity of method
if 20 ‰ discrimination gas to liquid:
1‰ uncertainty in keeling plot equates to 5% uncertainty of contribution
Uncertainties - d13C source signatures in Toronto
Potential bias/uncertainty:
Uncertainty in gas source signature of 4‰ translates to up to 16% bias of contribution
Uncertainty in all sources of 1‰ can cause a bias of up to 10% in contribution

## Slide 29
[Lopez et al. 2013 ACP]
Natural Gas
Liquid fuels
Solid fuels
Carbon-13
~ -39‰ to -41‰
~ -28‰ to 29.5‰
~ -24‰ to -25‰
Biogenic CO2
C3: -20‰ to -30‰
C4: -10‰ to -15‰
Winter
City-scale observation
Paris

## Slide 30: Observed d13Csource
GTA ≈ 60 Mt CO2
Bottom-up model (ICF 2008)
Night-time : -40.4‰ to -43.8‰
Night-time observation: -42.1± 0.7‰
Natural gas: 55±7% - Domestic heating, natural gas power plants
Liquid&solid fuels: 45±7% - Transportation, industrial processes & energy

## Slide 31
Chart: d13C in CO2 (permil, uncal)
d13C in CO2 observations in Toronto, Canada
Noticable instrumental drift over the course of months