## Slide 1: Multi-criteria evaluation of discharge simulation in Dynamic Global Vegetation Models (DGVMs) & The framework of our ecohydrological research
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Piao Group Ecohydrology Team
Author: Hui Yang et al.
Sponsor: Dr. Piao
Speaker: Zhenzhong Zeng
Notes: Good morning, everyone. Our topic today is multi-criteria evaluation of discharge simulation in Dynamic Global Vegetation Models. If there is enough time, we will also show the framework of our ecohydrological research. The first author of the discharge evaluation paper is Hui Yang. Nowadays, she is in France studying data assimilation technology. Instead, I am here doing this presentation. My name is Zhenzhong Zeng. Our sponsor is Piao Laoshi.

## Slide 2: Hui Yang (yang_hui@pku.edu.cn)
A grade one PhD student of Dr. Piao
Good at mathematics: undergraduate major mathematics
Study at ecohydrology and data assimilation.
First Author
Notes: OK. This is Yang Hui. I asked her to prepare a presentation introducing herself. But she rejected. So I do this presentation myself. I google this photo from Internet last night. You may meet her at LSCE when you are back Pairs.
Yang Hui is a grade one PhD student. Her undergraduate major is mathematics. Her future study might be ecohydrology and data assimilation.

## Slide 3: Multi-criteria evaluation of discharge simulation in Dynamic Global Vegetation Models (DGVMs)
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Piao Group Ecohydrology Team

## Slide 4
Background
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
(IPCC, 2013)
Water Cycle
Challenge
the scarcity and heterogeneity of river discharge measurements
4
Notes: River discharge is a main provision of water resources, and its variability and extremes, such as flood, can have large impacts on societies. Changes in the hydrological cycle associated with climate change include changes of surface discharge. Discharge future changes depend upon rainfall and snowfall changes, but also on altered evapotranspiration by vegetation and soils and the retention of water soils. All these components have different sensitivities to climate. Evapotranspiration and soil moisture are additionally affected by biogeochemical processes and by land use change and management. Natural and anthropogenic induced changes in river discharge and extreme hydrological events like drought and flooding are of a particular concern given their potentially damaging effects on human societies.
However, global knowledge of the river discharge is surprisingly poor, because much of the world river gauge measurements are rare, nonexistent or proprietary. To account for these processes and their interactions, land surface models fitted with an interactive vegetation component (DGVMs) are valuable tools. With DGVMs, all of the vegetation responses to climate change, rising atmospheric CO2, nitrogen deposition in some models, as well as to land use change, can be modeled.

## Slide 5
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Background
(IPCC, 2013)
Many studies use dynamic global vegetation models (DGVMs) to derive global discharge estimates. (e.g. IPCC AR5)
So far different DGVMs still cannot reach consensus on the attribution of continental discharge trends.
(Gedney et al., 2006; Piao et al., 2007)
(Gerten et al., 2008)
5
Notes: -DGVMs modeled discharge was used in IPCC Fifth Assessment Report. It can be used to quantitatively evaluate the separate contributions of different environmental factors to changes in regional and global discharge.
-So far different DGVMs still cannot reach consensus on the attribution of continental discharge trends. For instance, with the land surface scheme in Hadley Center climate models, Gedney et al. [2006] suggested that increasing atmospheric CO2 induced stomatal closure which in turn caused increasing global discharge over the period 19 century. While Piao et al. [2007] used the ORCHIDEE model and found a larger impact of rainfall increase and land use change on global positive discharge trends. Later, using the LPJmL model, Gerten et al. [2008] found that the increasing trend of global discharge was the result of multiple factor including precipitation changes, global warming, land use change, rising atmospheric CO2, and irrigation use of river water.
-Such differences in model prediction and attribution need to be systematically evaluated and compared for a better understanding of global and regional discharge under current and projected climate change and anthropogenic activities.

## Slide 6
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
TRENDY DGVMs
CLM4CN、LPJ、OCN、
LPJ-GUESS、SDGVM、
ORCHIDEE、TRIFFID
Global River Discharge Center (GRDC; in Koblenz, Germany, http://www.bafg.de/GRDC/)
DGVM
Observation
  Monthly runoff
  re-gridding into a 0.5o×0.5o grid
  1981-2010 period
Material and Methods
Simulation S2, an offline run where models were forced with
the same changing CO2 and climate
fixed (pre-industrial) land use.
  Daily discharge
Gauging stations locates in the estuary of river
  1981-2010 period
15 large river basins (>100,000 km2) over different continents except Africa
Route
The routing model converts simulated gridded runoff into river discharge at river mouths [Miller et al. 1994].
The global Dominant River Tracing (DRT)
a 0.5o by 0.5o grid
a 6-h time step
Notes: - In this study we used 7 DGVMs(CLM4CN、LPJ、OCN、LPJ-GUESS、SDGVM、ORCHIDEE、TRIFFID) from the TRENDY model inter-comparison project forced by the same observed climate and atmospheric CO2 data to investigate model performance in simulating basin level discharge.
- We evaluate the discharge outputs from seven DGVMs against river discharge observations in 15 large river basins(see Figure). Model comparison with observed discharge is decomposed into different time scales: the seasonal cycle, the annual mean discharge and its trend over last three decades, and the inter-annual variability.
In addition, DGVMs usually simulate the water balance of each grid cell. To compare with discharge observation, the monthly discharge simulated by DGVMs on each grid cell was fed into a river routing model. This routing model is the global Dominant River Tracing (DRT), it converts simulated gridded discharge into river discharge at river mouths.
Finally, we compare simulated river discharge to observed discharge. The observed river discharge data were obtained from the Global River Discharge Center on a daily basis from 718 stations. The gauging stations located in river mouths were selected for their close approximation of catchment discharge. We chose 21 gauging stations in the selected 15 river basins (see Figure). The analysis is focused on the period over the past thirty years.

## Slide 7
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Runoff simulation in DGVMs
Observed discharge
Annual mean discharge & its trend
Inter-annual variability
NSE
PBIAS
Corr.
Material and Methods
River discharge
Route
Compare
Seasonal cycle
RMSE
Skill score
the Epanechnikov kernel-based PDFs
Skill score
Corr.
the overlapping area
Notes: So, the discharge observation were compared to that from DGVMs.
We firstly directly compare model annual mean discharge & its trend against observations.
For seasonal cycle. We use multiple statistical indexes to evaluate seasonal discharge with emphasis on average mean bias (PBIAS), overall fitting (NSE), error index (RMSE) and agreement of variability (Correlation coefficient).
Then the these four evaluation are transformed to the associate score range from 0 to 1.
The average of the above four scores is considered to be the overall skill score which is used to qualify model performance of simulated seasonal cycle.
For inter-annual variability. Firstly, to check how models simulate the inter-annual variation of discharge, we calculated the correlation coefficients between detrended discharge simulations and observations. Secondly, we used another skill score to evaluate annual discharge, by comparing the Epanechnikov kernel-based probability density functions of models with reference values. This method is powerful, as it can show the discrepancy between simulated and observed data in both mean value and the inter-annual variability by calculating the common area under the two PDFs. For a perfect model simulation, the skill score would equal 1.

## Slide 8
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Seasonal Cycle
Notes: Here shows the results.
Left shows the seasonal cycle of both observed and model discharges. The black line is observation.
Right shows the Taylor diagram. The y-axis on the right panel shows the mean bias percentage of each model, and on the left panel reference data are plotted along the abscissa as a baseline. (1) The redial distance indicates the standard deviation. (2) The angle is proportional to the correlation coefficient. (3) The distance from the point of baseline is the centered RMSE. (4) And the color of point indicates the centered NSE (Nash-Sutcliffe Efficiency).
As shown in these figures:
In Tocantins and Amazon rivers, two South America river basins and also at low latitudes, most models could reproduce the seasonal cycle of discharge. SDGVM has the best performance among all models, with a small mean bias and the best match of the seasonal amplitude, the lowest RMSE and a high correlation coefficient (nearly 0.8) and NSE (nearly 0.5). In contrast, TRIFFID model has a poor performance.
In the mid latitudes, most models underestimate discharge for all months. It is particularly noticeable that all models have a poor performance in the Nelson River (in Canada). The results show a complex and large variability of models performances among different basins.
In the high-latitudes, observed discharge increases rapidly in April with snowmelt and then decreases slowly in June or July. Most models could not reproduce this seasonal cycle, especially for the Amur, Ob and Mackenzie rivers.

## Slide 9
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Seasonal Cycle
Yangtze
Yellow
Skill Score
Star Plot
The size of the sector indicates the seasonal skill score. The higher skill score is, the larger redial distance of sector will be.
Notes: Here is the skill score for seasonal cycle. In general, SDGVM has the best performance and TRIFFID the worst. However, different models perform differently in different latitudes, and no model is universally best across all river basins. The seasonal variation of discharge is well captured in the low and mid latitudes (average score of 0.6 between the models; ranging from 0.4 to 0.7), but not in the high latitudes.
In the low latitudes, the best scores are obtained for SDGVM and ORCHIDEE (average score of 0.7 for these two models) and the worst one for TRIFFID (score of 0.52). In the mid and high latitude basins, all the models have poor scores in the Amur, Nelson, Ob and Mackenzie, because of their poor performance in reproducing the seasonal variation.
In the Ob, Amur and Mackenzie River basins, the majority of the models cannot correctly reproduce the seasonal cycle. In the Lena, Yenisei and Yukon River, most models underestimate the peak discharge and overestimate spring discharge. A previous study showed the modeling of snow amount and timing of snowmelt is crucially important to determine the timing and magnitude of snowmelt discharge. Unfortunately, some DGVMs generally use a simplified water balance and discharge generation without snow accumulation and melt scheme.
The discharge seasonal cycle is also difficult to reproduce in arid or semiarid areas (e.g. Yellow River and Nelson River) given the low ratio of discharge to water withdrawals and damming, transmission loss, and evaporation from rivers and lake systems.

## Slide 10
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Annual Mean Discharge & its Trend
Notes: Here we show the annual mean discharge and its trend.
-In each subplot, y axis indicates mean annual discharge and the error bar indicates its standard deviation, x axis indicates the long-term trend of discharge estimated by linear regression. Different dots representing observed (Black) and model simulated data (color).
These three basins are in low latitudes. These five basins are located in high latitudes.
-For the mean annual discharge, generally, most models underestimate annual mean discharge. The overall underestimate of annual discharge by the 7 DGVMs forced by the same climate data may also reflect to systematic uncertainties in the forcing climate data. And the availability and reliability of observed data vary from one river basin to another, and the differences between observed and simulated discharge of different basins may be relevant to the configuration of gauging stations and uncertainties in the rating curves.
- The observed trend is generally positive in most of the high and mid latitude river basins except for Amur, Yangtze and Yellow River, while it is negative in the low latitudes. The sign of the trends in discharge can be reproduced by most models except for the Yukon River. But the magnitude of trends is generally under-predicted. A previous study showed that warming may increase peak discharge due to a larger snowmelt. The warming induced increase in peak discharge is not captured by the DGVMs. Increasing human water uses through dams and irrigation likely induce the decreasing trend in Yangtze River, Yellow River and Amur. Those effects, however, have not been not fully considered in most DGVMs.

## Slide 11
Inter-annual Variability
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Correlation Coefficients
Skill Score
Notes: Here is the interannual variability.
-The left figure is the correlation coefficients between interannual variation of observed discharge and model discharge. It shows that most models capture the inter-annual discharge variability, but the correlation coefficient values remain lower in some high latitude basins and the Amazon basin.
-The right figure is the skill score matrix of the inter-annual variability of discharge. It indicates an overall low score for OCN, especially in the mid and high latitudes. LPJ-GUESS has good performances in some mid latitude basins and gets the highest score in the Yangtze River basin. In general, the performances of ORCHIDEE, CLM4CN and TRIFFID are not the worst but also not the best.
-The inter-annual variability as well as seasonal cycle of simulated discharge data in the tropics and the high latitudes seems to be problematic. In line with earlier studies, in the tropical regions the deficiencies of the models in reproducing the decadal variations are likely caused by poor availability and quality of climate forcing data.

## Slide 12
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Limitations and Uncertainties
Runoff simulation in DGVMs
Observed discharge
River discharge
Route
Compare
Source of Uncertainties
Scale mismatch and uncertainty in observed discharge
Bias and uncertainty in forcing data
(temperature and precipitation inputs，fixed land use)
uncertainties in the physical construction of DGVMs
uncertainties in river routing process
Indispensable process especially on the large river
Improve the discharge simulation in most case
12
Notes: Of course, our approach here has some limitations and uncertainties. The source of uncertainties include: …
-Here the observed discharge records are from the gauging stations that are located at the river mouths, and a river routing model was applied to convert gridded simulated discharge to discharge. It has been suggested that river routing models are indispensable when focusing on the seasonality of discharge especially on the large rivers. In most cases, with a river routing results into an improvement of the discharge simulation of DGVMs.(see next slide)

## Slide 13
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Limitations and Uncertainties
uncertainties are driven by the parameterization(flow velocity) of river routing processes
Uncertainties in river routing process
with routing Vs without routing
(Ringeval et al., 2013)
the Miller routing model only considers the routing scheme in surface runoff.
the discharge of some DGVMs might be calibrated without considering a river routing scheme
13
Notes: -Bad performance after river routing only appears in Mississippi, Amur, Ob and Mackenzie River
-This bias is most likely due to the river routing model. One uncertainty is driven by the parameterization(flow velocity) of river routing processes. We applied Global Dominant River Tracing in this study, in which the time-independent flow velocity is parameterized as a function of the topographic gradient. Using another routing scheme with different time-independent flow velocity, Ringeval et al. (2012) obtained a better discharge values through the ORCHIDEE model for Russian rivers.
- For Mississippi, we found that the change of land use is probably accelerating the river flow. In fact, in the TRENDY Simulation S2 DGVMs were forced with fixed (pre-industrial) land use. Therefore, if DGVMs were forced with the changing land use, the simulated discharge without routing would be earlier than the observations and the simulated discharge with routing would be closer to the observations.

## Slide 14: The framework of our ecohydrological research
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014
Piao Group Ecohydrology Team
Hydrology:
Precipitation
Evapotranspiration
Soil moisture
Runoff, water yield
Ecology:
NDVI, LAI
Tree height, Tree cover
GPP, NPP, NEP

## Slide 15: ET is a nexus; Water yield is available refresh water
Water Cycle
Energy Cycle
Trenberth et al., 2009 BAMS
Oki et al., 2006 Science
Trading water
for carbon
Jackson et al., 2006 Science
Carbon Cycle

## Slide 16: Stage One: What do we trust?
Observation, observation and observation
We gathered plenty related dataset:
Precipitation: Gauging station, CRU, GPCC, …
Runoff: Gauging station
ET: Jung et al., MOD16, Zhang et al., Fisher et al
Soil moisture: EVC, ERA
Vegetation: satellite-derived index (NDVI, LAI, tree cover ……)
……
We desire more, particularly long-term station observation
Stage 1: Observation

## Slide 17: Global grid Runoff Dataset
There is no observed global grid runoff dataset. And it is impossible to observe it.
Land surface model is the only tool to estimate this dataset.
Thus we want to estimate global grid runoff dataset integrated with models and gauging station discharge using Bayesian method.
We do not directly finish this job, because we do not regard all model as equally good in its performance. So we evaluate those models at the beginning.
Next step is to project global grid runoff dataset with weight varying model and region. Yang Hui has finished the whole job now and is preparing the manuscript.]. Once the paper is published, our datasets will be released 
Stage 1: Observation

## Slide 18: Global grid ET dataset
Many dataset since 2008, but all bottom-up approaches. There is large uncertainty!!!
We designed a top-down approach to estimate global grid ET dataset over the past thirty years.
Wahr et al., 1998 JGR
Stage 1: Observation

## Slide 19
Stage 1: Observation
Zeng et al., 2012 ERL
Cited by IPCC AR5 
Zeng et al., 2014 JGR
This dataset has released at the website :
http://www.lmd.jussieu.fr/~zzlmd/PKU/

## Slide 20
Rodel et al., 2004 GRL
Zeng et al., 2012 ERL; 2014 JGR
ET(n)=P(n)-R(n)-TWSC(n)
TWSC(n)=TWSA(at the end of period n)-TWSA(at the start of period n)
ET: evapotranspiration; P: precipitation; R:runoff;
TWSA(c): anomaly (change) of terrestrial water storage
Stage 1: Observation

## Slide 21
We will never satisfy with the observation. Hence the stage one will never stop.
In the second stage, combined with these observation-based dataset and model simulations, we will focus on urgent and classic ecohydrological problems.
Stage 1: Observation

## Slide 22: Stage Two: What is happening or will be happened?
Water Use Efficiency (WUE)
Water Yield and vegetation
ET sensitivity to precipitation and vegetation
Partitioning precipitation to ET, runoff and terrestrial water
Vegetation-climate (water budget) interaction, vegetation role during drought
Water cycle intensification: Why, How, and drivers
Cease of the water cycle intensification (in particular ET): Climate change signal for a switch in behavior or natural climate oscillation
……
Stage 2: Science

## Slide 23: Water Use Efficiency (WUE)
Mengtian and Yan will give this presentation tomorrow.
Stage 2: Science

## Slide 24: Water Yield
An example: We defined tree cover is maximum potential tree cover when water yield reaches zero.
Zeng et al., 2013 Scientific Report
Many works need to be done related to water yield!!!
Stage 2: Science

## Slide 25: ET sensitivity
The striking difference between different ET product is its sensitivity to precipitation and vegetation index (e.g. NDVI).
Stage 2: Science

## Slide 26: Partitioning precipitation
A classic ecohydrological problem has not been answered.
Stage 2: Science

## Slide 27: Water cycle intensification
Water cycle intensification over the past three decades.
What is the driver?
Does the intensification water cycle cease.
Why it cease? Climate change signal for a switch in behavior or natural climate oscillation
Come back to the driver, within the land system?
……
Stage 2: Science

## Slide 28
Temperature change
Precipitation change
Vegetation (NDVI) change
Relative humidity change
Change in the same direction!

## Slide 29
Jung et al., 2010 Nature
Diego et al., 2013 NCC
Climate change signal for a switch in behavior or natural climate oscillation ?

## Slide 30: Thank you!
Third Spring School PKU-LSCE on Earth System Science
May 12-16 2014