## Slide 1: High-resolution N2O emission inventory of China Feng Zhou, Wei Gao, Qiong Chen, Han Chen, Shu Tao, Shilong Piao, Hongyan Liu College of Urban and Environmental Sciences Peking University, P. R. China Sino-France Workshop on Radiactive Forcing October 1, 2012, Paris

## Slide 2: Content
Background of N2O emissions in China
Data and methods
Preliminary results
Conclusions and future work

## Slide 3: 1. Background
N2O is 3rd important GHG and a key role in destruction of the ozone layer through formation of NOx, leading to climate radiactive forcing (Reis et al., 2011; Reay et al., 2012)

## Slide 4: 1. Background
However, a fair amount of research has been conducted an N2O emission inventory of world or China (EDGAR v4.2, 2009; IIASA, 2008; Li and Lin, 2000; Chen et al., 2009).
EDGAR v4.2
IIASA’S GAINS

## Slide 5: 1. Background
Problem I: Activity data is too coarse (National or province), leading to low spatial-resolution (EDGAR v4.2, 2009; IIASA, 2008; Zheng et al., 2004, 2008; Chen et al., 2009; Gao et al., 2009)
Problem II: Emission factors is too scarce in developing countries, resulting in low reliability and large variations (0.4-10.8 Tg for China) (Chen et al., 2009; Ji et al., 2011; Zhao et al., 2012)
Problem III: Emission sources are a bit incomplete, leading to some misunderstanding of N2O source apportionment (Li et al., 2011; Tian et al., 2011; Xu et al., 2008; Gu et al., 2009; Zhuang et al., 2012)

## Slide 6: 1. Background
So, it is greatly essential to update and re-assess N2O emission inventory by using
Local values of emission factors (EFs)
County-based activity datasets for
All of emission sources
China (2008)

## Slide 7: 2. Data and methods
2.1 Computational approach
where
i: Emission source, i=16;
j: County or grid, j=2,378 or 0.10.1
k: Condition, i.e., slope, land use, crop type, region

## Slide 8: 2. Data and methods
2.2 Source i
Direct from soils or industries
Indirect by precursors or leach/runoff

## Slide 9: 2. Data and methods
2.2 Source i
V
D1: Fertilizer
D2: Organic
D3: Manure in PRP
D4: Crop residue
D5: N-mineralized
D7: Manure management
D9~14
Energy &
Chemical
V
D6: Wastewater
15: deposition
V
16: Leach & Runoff
D8:Histosol

## Slide 10: 2. Data and methods
Source | Resolution | References
D1 Synthetic fertilizer D2 Organic fertilizer D3 Manure in PRP D4 Crop residues D7 Manure management | county | Statistical Yearbook of each city (362) China Industry Statistical Yearbook China’s county Statistical Yearbook (>2000)
D9 Chemical Industry | Point+ Province | 
D6 Wastewater handling | 1*1km | Urban population from RESDC (CAS)
D5 N-mineralization in Soil | 0.5*0.5 | SOC derived by LPJ, LPJ-GUESS, and ORCHIDEE models Harmonized World Soil Database, 2011
D8 Histosols management | 1*1km | 

## Slide 11: 2. Data and methods
Source | Resolution | References
D10 Public electricity and heat production D11 Manufacturing Industries and Construction D12 Residential and other sectors D13 Road transportation | 0.1*0.1 | Wang et al., 2012 in ES&T Wang R., 2012 in ACP
D14 Rail transportation | 1*1km | China Railway Statistical Yearbook for province
D15 NH3 | 1*1km | Huang et al., 2012 GBC EDGAR v4.2, 2008
D15 NOx | 0.1*0.1 | 
D16 Leaching and runoff | -- | Same as D1~D5

## Slide 12: 2. Data and methods
2.3 Activity dataset at place j of source i
Source | Activity data
D1 Synthetic fertilizer | N-fertilizer, Compound fertilizer,
D2 Organic fertilizer | Exceations from Cattle, Dairy cattle, Sheep, Pig, Poultry, Others, Rural population
D3 Manure in PRP | Cattle, Dairy cattle, Sheep, Pig, Poultry, Others
D4 Crop residues | Rice, Wheat, Barley, Maize, Soybean, Potato, Oil plant, Peanut, Millet, Sorghum, Alfalfa, Others
D5 N-mineralization in Soil | Changes of SOC
D6 Wastewater handling | Urban population

## Slide 13: 2. Data and methods
2.3 Activity dataset at place j of source i
Source | Activity data
D7 Manure management | Cattle, Dairy cattle, Sheep, Pig, Poultry, Others
D8 Histosols management | Area of Land use under different temperature and nutrient availability
D10~14 All type of Energy | Oil, Gas, Coal, Biomass, Waste
D15 NH3 and NOx | NH3 and NOx emission rates
D16 Leaching and runoff | Same as D1~D5

## Slide 14: 2. Data and methods
2.4 EFs for source i at place j under condition k
Source | EFs | Determined by
D1-D5, D15 | EF1 | Site-specific from papers
D8: Histosols management | EF2 | IPCC’s
D7 | EF3 | Site-specific from papers
D6 | EF4 | Site-specific from observation
D16 | EF5 | Site-specific from observation
D9: Chemical industry | EF6 | IPCC’s
D10-D14: Energy | EF7 | IPCC’s

## Slide 15: 2. Data and methods
Region | type | mean | Range
Xinjiang, Qinghai, Xizang, Shanxi, Gansu, Shaanxi, Inner Mongolia, and Ningxia | Upland | 0.006 | 0.0017-0.01
 | Paddy | 0.003 | 0.0002-0.009
Heilongjiang, Jilin, and Niaoning | Upland | 0.013 | 0.0027-0.031
 | Paddy | 0.005 | 0.0003-0.013
Beijing, Tianjing, Hebei, Henan, Shangdong | Upland | 0.006 | 0.0017-0.01
 | Paddy | 0.003 | 0.0002-0.009
Zhejiang, Shanghai, Jiangsu, Anhui, Jiangxi, Hunan, Hubei, Sichuan, Chongqing | Upland | 0.015 | 0.0059-0.027
 | Paddy | 0.005 | 0.0004-0.015
Guangdong, Guangxi, Hainan, Fujian | Upland | 0.021 | 0.0091-0.033
 | Paddy | 0.007 | 0.0003-0.021
Yunnan and Guizhou | Upland | 0.014 | 0.0047-0.026
 | Paddy | 0.006 | 0.0005-0.017
EF1: Zheng et al., 2004, 2008; Gao et al., 2011; Xing, 1998; Xing and Yan, 1999; Xing and Zhu, 2000; Yan et al., 2003; Li et al., 2003; Zou et al., 2009, 2010

## Slide 16: 2. Data and methods
Management system | mean | Range
Slurry | 0.0217 | 0.0197-0.0237
Solid storage | 0.0217 | 0.0197-0.0237
Dry lot | 0.005 | 0.0027-0.01
PRP for Cattle, Pig, Poultry | 0.0217 | 0.0197-0.0237
PRP for Sheep and others | 0.011 | 0.009-0.014
EF4 | 0.0035 | 0.0029-0.0041
EF3 and EF4: Lu et al., 2007; Xie et al., 2003; IPCC, 2006; Hiscock et al., 2002, 2003; Reay et al., 2004, 2005; Sawamoto et al., 2005; Wang et al., 2012

## Slide 17: 2. Data and methods
EF5: Ju et al., 2009; Tian et al., 2007; Peng et al., 2011; Ji et al., 2011; Zhao et al., 2012; Lv, 1999; Zhu et al., 2004; Li et al.,, 2008; Li et al., 2009; Xing and Zhu, 2000; Yi and Xie, 1993; Dai and Zhao, 1992; Yuan et al., 1995; NEP, 2009; Zhang et al., 1986; Li, 1989; Zhang et al., 1986
372 leaching/ runoff experiment area of different cropland in 6 regions in 2008, (National Pollution Sources Survey Project)
including 140 for leaching and 232 for runoff

## Slide 18: 2. Data and methods
EF5:
Region | Slope | Cropland | Mean | interval
Xinjiang, Qinghai, Xizang, Shanxi, Gansu, Shaanxi, Inner Mongolia, Ningxia | Steep | Upland | 0.015 | 0.003-0.029
 | Steep | Paddy | -- | --
 | Slow | Upland | 0.017 | 0.003-0.032
 | Slow | Paddy | -- | --
 | Flat | Upland | 0.016 | 0.003-0.031
 | Flat | Paddy | 0.003 | 0.002-0.003
Heilongjiang, Jilin, Liaoning | Steep | Upland | 0.004 | 0.003-0.029
 | Steep | Paddy | -- | --
 | Slow | Upland | 0.006 | 0.003-0.032
 | Slow | Paddy | -- | --
 | Flat | Upland | 0.005 | 0.004-0.031
 | Flat | Paddy | 0.005 | 0.005-0.006
Beijing, Tianjing, Hebei, Henan, Shangdong | Steep | Upland | 0.015 | 0.003-0.029
 | Steep | Paddy | 0.000 | 0-0
 | Slow | Upland | 0.017 | 0.003-0.032
 | Slow | Paddy | 0.000 | 0-0
 | Flat | Upland | 0.018 | 0.006-0.034
 | Flat | Paddy | 0.012 | 0.011-0.013

## Slide 19: 2. Data and methods
EF5:
Region | Slope | Cropland | Mean | interval
Zhejiang, Shanghai, Jiangsu, Anhui, Jiangxi, Hunan, Hubei, Chongqing | Steep | Upland | 0.015 | 0.012-0.023
 | Steep | Paddy | 0.016 | 0.004-0.031
 | Slow | Upland | 0.018 | 0.012-0.025
 | Slow | Paddy | 0.017 | 0.005-0.032
 | Flat | Upland | 0.018 | 0.015-0.023
 | Flat | Paddy | 0.017 | 0.006-0.03
Guangdong, Guangxi, Hainan, and Fujian | Steep | Upland | 0.015 | 0.012-0.023
 | Steep | Paddy | 0.016 | 0.004-0.031
 | Slow | Upland | 0.018 | 0.012-0.025
 | Slow | Paddy | 0.017 | 0.005-0.032
 | Flat | Upland | 0.018 | 0.015-0.023
 | Flat | Paddy | 0.017 | 0.006-0.03
Yunnan and Guizhou | Steep | Upland | 0.015 | 0.012-0.023
 | Steep | Paddy | 0.016 | 0.004-0.031
 | Slow | Upland | 0.018 | 2.146-3.761
 | Slow | Paddy | 0.017 | 0.877-4.908
 | Flat | Upland | 0.018 | 2.827-3.436
 | Flat | Paddy | 0.017 | 1.175-4.501

## Slide 20: 2. Data and methods
2.5 Spatial allocation from county-based to 11 km based on correlation analysis and previous experiences
Source | Allocation proxy
D1, D2, D4 | 1*1 km cropland
D3 | 1*1 km grassland
D7 | 1*1 km Rural population
D16 | Same as D1~D5
D5, D6, D8, D10~D15 | Origin are raster-based (1*1km, 0.1*0.1, or 0.5*0.5 )

## Slide 21: 3. Preliminary results
1: This study
2. http://edgar.jrc.ec.europa.eu
3. http://gains.iiasa.ac.at
Local EFs with new ADj 1 | IPCC's EFs with new ADj 1 | EDGAR v4.2 (IPCC's Efs) 2 | IIASA China (IPCC's Efs) 3
1665.4 Gg (880-3,146 Gg) | 1773.8 Gg (394-10,839 Gg) | 1760.0 Gg | 1998.8 Gg
3.1 Total N2O emissions in this study is a little smaller than previous results

## Slide 22: 3. Preliminary results
3.2 Source apportionment (Gg) with uncertainty
Type | Local EFs with new ADj 1 | IPCC's EFs with new ADj 1 | EDGAR v4.2 (IPCC's Efs) 2 | IIASA China (IPCC's Efs) 3
Direct: Agriculture | 1236.6 (679-2022) | 1133.1 (244-3085) | 980.0 | 1697.8
Direct: Energy | 161.1 (59.2-575) | 161.1 (59-575) | 174.0 | 132.3
Direct: Waste | 73.0 (60.5-85.5) | 104.3 (10.4-5215) | 67.8 | 135.8
Direct: Chemical Industry | 52.8 (35.3-76.1) | 52.8 (35.5-76.1) | 193.7 | 42.5
Indirect: Precursors | 115.3 (34.8-317) | 147.3 (36.1-429) | 348.9 | --
Indirect: Leach & Runoff | 26.6 (11.4-70.1) | 175.2 (9.2-1459) |  | --

## Slide 23: 3. Preliminary results
3.2 Source apportionment (Gg)
IPCC’s
Local
D1
D7
D6
15
16

## Slide 24: 3. Preliminary results
3.3 Spatial distribution: Total emissions
Unit:
Kg N2O/km2/yr

## Slide 25: 3. Preliminary results
3.3 Spatial distribution: IPCCTotal−LocalTotal
Unit:
Kg N2O/km2/yr
Northwest 
North Plain 
Northeast 
Southern 

## Slide 26: 3. Preliminary results
3.3 Spatial distribution: Comparison for provinces
76% 
62% 
58Gg, 57% 
49%
32Gg, 47% 
46% 
38Gg, 42% 
-22Gg, -27% 

## Slide 27: 3. Preliminary results
3.3 Spatial distribution: Comparison of fertilizer (D1)
Local
IPCCLocal
North Plain 
Southern 

## Slide 28: 3. Preliminary results
3.3 Spatial distribution: Province comparison
Direct: Synethic fertilizer (Gg/yr)
24Gg, 65% 
24Gg, 65% 
-21Gg, -34% 
-11Gg, -34% 
-18Gg, -53% 
-14Gg, -53% 
6.7Gg, 66% 

## Slide 29: 3. Preliminary results
3.3 Spatial distribution: Wastewater handling
Local
IPCCLocal






## Slide 30: 3. Preliminary results
3.3 Spatial distribution: Province comparison
Direct: Wastewater handling (Gg/yr)
3.4Gg 
2.4Gg 
2.7Gg 
2.2Gg 

## Slide 31: 3. Preliminary results
3.3 Spatial distribution: Precursors
Local
IPCCLocal
North Plain 

## Slide 32: 3. Preliminary results
3.3 Spatial distribution: Province comparison
Indirect: Precursor (Gg/yr)
7.8Gg, 65% 
-6.3Gg, -54% 
5.3Gg, 67% 
6.5Gg, 65% 
-3.5Gg, -37% 
-3.6Gg, -35% 

## Slide 33: 3. Preliminary results
3.3 Spatial distribution: Leaching and runoff
Local
IPCCLocal

## Slide 34: 3. Preliminary results
3.3 Spatial distribution: Province comparison
Indirect: Leaching & Runoff (Gg/yr)
142%~2328% 

## Slide 35: 3. Preliminary results
3.3 Spatial distribution: Organic Fertilizer source
Local
IPCCLocal




## Slide 36: 3. Preliminary results
3.3 Spatial distribution: Province comparison
Direct: Organic fertilizer (Gg/yr)
5.1Gg, 67% 
-3.6Gg, -23% 
2.4Gg, 67% 
2.4Gg, 67% 
-3.8Gg, -33% 

## Slide 37: 4. Conclusions and future work
Amount: Total N2O emissions is 1665.4 Gg with range of 880-3,146 Gg, which is a little smaller than previous results.
Source contribution: Agricultural source is underestimated, while wastewater handling and indirect types are significantly overestimated using IPCC
Spatial distribution: North Plain and western China are overestimated, while Northeast and Southern China are underestimated using IPCC

## Slide 38: 4. Conclusions and future work
Uncertainty analysis: More detailed analysis will be pursued for both ADs and EFs
Atmospheric inversion for N2O??

## Slide 39: Thank you Question?