## Slide 1
30 years of methane : from global to regional
P. Bousquet, S. Kirschke, M. Saunois, P. Ciais, P. Peylin,
R. Locatelli, I. Pison, B. Ringeval, C. Prigent, F. Chevallier, et al.
SOFIE workshop, Oct 2nd, 2012.

## Slide 2
Evolution of atmospheric methane (surface)
NOAA, ESRL
High growth rate period
< 1991
Lower growth rate period
1991-1996
Stabilisation period
1999-2006
El Niño
1997-1998
Pinatubo,
USSR collapse
1991-
Recent increase
2007-?
Relative minimum
in 2005-06

## Slide 3: Methane table in the IPCC 2007
Denman et al., 2007

## Slide 4: GCP Global Methane Synthesis
The scientific goal of the global carbon project is to develop a complete picture of the global carbon cycle
Starting point : no regular and consistent budget for methane as for CO2.
Regular update of the CH4 global budget, annually or bi-annually – similar to global CO2 budget
Synthesis of bottom-up and top-down studies
 Contributions from :
  Observational networks (NOAA, CSIRO, LSCE, AGAGE)
  Inventories (EDGAR, GFED, GICC, FINN, IIASA, EPA)
  Inverse modeling groups, chemical-transport models and chemistry-climate models (OH)
  Process-based models for wetland and biomass burning
 Regular budget release in collective papers

## Slide 5: General approach
Bring together Top-Downs inversions (8) and Bottom-Up models (5) and inventories (4)
Address decadal means (80s, 90s, 00s), inter-annual variability, trends, and uncertainties
Global to (broad) regional scales
Include all studies with more than 5 years at global scale to represent one decade
Published work, updates, and new studies
Consistent analyses of the submitted data for emissions and sinks

## Slide 6: Decadal Budget Table
Kirschke et al., 2012

## Slide 7: Agreement on Decadal CH4 emissions
Kirschke et al., 2012
The Dalmatian plot :

## Slide 8: Regional Methane Budgets
Contributors:
ORCHIDEE (Ringeval et. al., 2010)
LPJ-WHy-Me (Spahni et al., 2011)
LPJ-WSL (Hodson et al., 2011)
GFEDv2 (van der Werf et al. 2006)
GFEDv3 (van der Werf et al. 2010)
RETRO (Schulz et al. 2007)
GICC (Mieville et al. 2010)
FINN (Wiedinmeyer et al. 2011)
EDGAR (European Comission, 2010)
IIASA (Dentener, 2005)
EPA (EPA, 2011)
Bousquet et al., 2011
Bruhwiler et al. (in prep.)
Houweling et al. (in prep.)
Fraser et al. 2011
Bergamaschi et al. (2009, 2010)
ACCMIP (in prep.)
Kirschke et al., 2012

## Slide 9: Surface Fluxes (as computed by land surface models and inventories)
Kirschke et al., 2012

## Slide 10: Interannual Variability of the CH4 emissions
Kirschke et al., 2012

## Slide 11: Processes explaining flux anomalies
Pison et al., in prep
Monthly anomalies of CH4 wetland emissions, precipitations and temperature in Tropical South America

## Slide 12: Regions explaining flux anomalies
Pison et al., in prep
INVERSION
ORCHIDEE

## Slide 13: Processes explaining flux anomalies
Pison et al., in prep
Monthly anomalies of CH4 wetland emissions, precipitations and temperature in Tropical South America

## Slide 14: IAV of the CH4 chemical loss per latitude band (1°)
1990s
2000s
Kirschke et al., 2012

## Slide 15: Take-home messages
A first assessment of the decadal methane budget for the 80s, 90s and 00s
More consistent anthropogenic decadal emissions than natural ones
The uncertainties in natural wetland mean emissions limit our ability to fully close the CH4 budget
Probably too large global emissions inferred by bottom-up approaches (no atmospheric constraint)
Little ability of the T-D inversions to partition emissions among source types
Still large uncertainties on decadal means but reduced compared to AR4 spread
IAV dominated by natural wetlands (year-to-year), with short-term impacts of biomass burning. More robust than decadal means.
Contradictory trends in fossil fuel, agriculture, and waste and natural wetlands for the 2000s
Improved agreement for a small OH IAV in the 2000s between T-D and B-U
South America is a key region to study
Recent changes still debated !

## Slide 16: Future directions (1) : Isotopes
What is the interest of dD and d13C in CH4 ?
Double isotopic signature of various sources of methane determined by experimental studies. Adapted from Marik 1998.

## Slide 17: Future directions (1) : Isotopes
Inter-hemispheric difference of 13CH4 observations
Kai et al.,2011
Levin et al., 2012

## Slide 18: Future directions (2) : Transport model errors
Transcom-CH4 models’ outputs are used as pseudo observations at 160 surface stations
The variational inversion system (PYVAR-LMDZ) is used to compute the inversions (Chevallier at al., 2007)
The INV emission scenario from Patra et al. (2011) is used as a priori scenario
Pseudo Observations
INV emission scenario
INVERSION SYSTEM:
PYVAR
Estimated CH4 fluxes
Locatelli, et al., in prep
TransCom-CH4 models outputs

## Slide 19: Future directions (2) : Transport model errors
CCAM
PCTM
Locatelli, et al.,
in prep
ppb
Atmospheric
differences

## Slide 20: Future directions (2) : Transport model errors
USA
Europe
Africa
South Asia
Continental inverted fluxes
Locatelli, et al., in prep

## Slide 21: CH4 Atmospheric Growth Rate, 1983-2009
Kirschke et al., 2012