# mSATA notes
DANGER! NEVER disable the mSATA disk in the BIOS if the main disk has not been synchronized. Otherwise, the main disk will appear as damaged and will have to be completely re-installed…

IMPORTANT If you change the partitions with gparted, leave some empty space (4-8 Mb) at the end of the disk, otherwise you will not be able to re-activate the disk acceleration…

## What is mSATA?
A mSATA disk is a small (e.g. 32 Gb) SSD disk that is installed on a machine in order to be used in combination with a regular (i.e. bigger) disk:
- as a fast system disk
- as a fast cache to accelerate the regular disk
## Low level mSATA administration
It is possible to enter the low level interface by typing CTRL-I when the machine is booting. You will then be in the Intel (R) Rapid Storage Technology - Option ROM interface
Note: on HP machines, the use of CTRL-I at boot time must be enabled in the BIOS
### Synchronizing the cache and the disk
Select Acceleration Options, then type 's' to synchronize the disk. The Status must be In Sync
### Disabling the acceleration
### Enabling the acceleration
## mSATA administration in Windows
Everything is done in the Intel Rapid Storage Technology program
Start menu ⇒ All programs ⇒ Intel ⇒ Intel Rapid Storage Technology
### Disabling the acceleration
You have to disable the acceleration before you use GPARTED!

Performance ⇒ Désactiver l'accélération
### Enabling the acceleration
## Misc. notes
In order to use the mSATA for cache/acceleration, the following setting has to be activated in the BIOS
(Dell) Settings ⇒ System Configuration ⇒ SATA Operation: RAID on

[ PMIP3 Wiki Home ] - [ Help! ] - [ Wiki syntax ]